## Slide 1
BIRDI RESEARCH
Evolution
Current System
Evidence
Next Steps
Evolution of the BIRDI research pipeline
From latent structural learning to explicit plans and executable verification
BIRDI | Research evolution
From graph-latent learning to verified RTL generation
1 / 2
1. Graph-latent Python
AST + state/data-flow graph latent
code graph -> JEPA alignment -> graph decoder -> Python
WHAT WE RETAINED
Structural supervision and contrastive alignment can organize problem and solution representations.
WHY WE EVOLVED
The decoder drifted semantically; small prompt changes could produce the same incorrect logic.
2. Typed IR + retrieval
Compact typed algorithm DSL / IR
JEPA latent -> top-k IR -> CodeT5+ repair -> compiler
WHAT WE RETAINED
An explicit target made retrieval, repair, and final code generation separately diagnosable.
WHY WE EVOLVED
Algorithm composition remained limited when prototypes and repair training lacked the needed variation.
3. Verified RTL agents
Verilog + executable oracle evidence
RTL -> generated tests -> Icarus -> repair -> benchmark
WHAT WE RETAINED
Compilation, simulation, mismatch traces, and repair connect model output to measurable behavior.
WHY WE EVOLVED
Random stimuli may miss rare states, and two agents can still agree on the same wrong behavior.
Design principle carried forward
We progressively reduced hidden inference: latent graph -> explicit typed IR -> executable behavioral evidence.

## Slide 2
BIRDI RESEARCH
Evolution
Current System
Evidence
Next Steps
Current implementation: verify and repair before final scoring
The same RTL generator is evaluated under two oracle-family conditions
BIRDI | Research evolution
From graph-latent learning to verified RTL generation
2 / 2
Executable multi-agent RTL workflow
RTL specification
Ports, timing, and required behavior
RTL generator
Qwen2.5-Coder-7B candidate Verilog
SHARED
Oracle package
Generated SV tests and reference intent
QWEN / DEEPSEEK
Icarus checks
Compile and simulate candidate behavior
Repair
On compile failure or oracle mismatch
Official scoring
Final VerilogEval pass@1
EVALUATION ONLY
Preliminary VerilogEval pass@1 | 50 complexity-weighted tasks
Verification and repair produced the largest observed gain.
Single RTL agent
baseline
52%
Different-family oracle
+6 pp
58%
Same-family oracle
+8 pp
60%
Preliminary subset result; denominator = 50 attempted tasks.
Interpretation and next experiment
1
Verification adds measurable value
Both oracle variants improved the same generator's final pass@1.
2
Family diversity was not automatically superior
Qwen oracle reached 60% vs DeepSeek at 58%; capability mattered more in this run.
3
Strengthen evidence beyond agent agreement
Next: directed + metamorphic tests, coverage feedback, bounded formal checks, and executable cycle-accurate Python references.